## Slide 1: Visual Vibrometry: Estimating Material Properties from Small Motions in Video
Presented by Deblina Bhattacharjee
Intelligent Media Research Centre, Postech- Samsung
, , , ,

## Slide 2: Visual Vibrometry
Intelligent Media Lab @ POSTECH
Approach
Presents a technique to estimate material properties for objects with fixed or known geometry from small motions in video.
Solid objects tend to vibrate at a set of preferred frequencies.
These vibrations occur at frequencies outside the range of human visual perception.
These vibrations can be recovered from video, even for motion smaller than 1 pixel.

## Slide 3: Overview
Intelligent Media Lab @ POSTECH
A method to estimate material properties of an object by examining small motions in video.
Local motion signals are extracted from captured videos and used to compute a temporal power spectrum for each object.
The temporal frequencies of motion in the spectrum is used to find resonant frequencies of visible objects.
Frequencies of these modes can be directly related to its material properties.
Here, resonant frequencies are
mode shapes are
Video
From eigenmode analysis

## Slide 4: Motion Extraction
Intelligent Media Lab @ POSTECH
Using complex valued steerable pyramids of the image, the local phase variations in every spatial sub-band of the image is extracted which gives the motions in these spatial image sub-bands.
Orientation 2
Real
Imag
Scale 1
Orientation 1
Scale 2
Orientation 1
Orientation 2
Bandpass Filters iterations

## Slide 5: Complex Steerable Pyramid
Intelligent Media Lab @ POSTECH

## Slide 6: Complex Steerable Pyramid
Intelligent Media Lab @ POSTECH
High-pass filter
Low-pass filter
Band-pass filter
synthesized signal
Subsampling (downsampling)
signal
... (recursively defined)

## Slide 7: Complex Steerable Pyramid Basis Functions
Intelligent Media Lab @ POSTECH
Window
Intensity
Space (x)
Complex Sinusoid (Global)
Intensity
Space (x)
Space (x)
Intensity

## Slide 8: Local Amplitude
Intelligent Media Lab @ POSTECH
Local amplitude controls strength of basis function
Single Sub-band of Image Profile
Local Amplitude

## Slide 9: Local Phase Shifts
Intelligent Media Lab @ POSTECH
Single Sub-band of Image Profile
Local Phase
Local Motions
Local phase controls location of sinusoid under window, approximates local translation

## Slide 10: Complex Steerable Pyramid Decomposition
Intelligent Media Lab @ POSTECH
Amplitude
Sub-bands
Filter Bank
Orientation 2
Real
Imag
Scale 1
Orientation 1
Scale 2
Orientation 1
Orientation 2
Phase
Amplitude
Phase
Bandpass Filters iterations

## Slide 11: Phase Over Time
Intelligent Media Lab @ POSTECH
Amplitude
Sub-bands
Filter Bank
Orientation 2
Real
Imag
Scale 1
Orientation 1
Scale 2
Orientation 1
Orientation 2
Phase
Temporal Filtering
Local Phase Variation calculated below gives the motion estimation.

## Slide 12: Motion Extraction
Intelligent Media Lab @ POSTECH
Let: be amplitude and be the phase function of input signal.
Motion signal can be generated using phase variation of the complex steerable pyramid of image.
The local motion is computed by summing the square of amplitude in pyramid w.r.t phase difference.
Spatial Filtering the above signal for removing noise.

## Slide 13: Motion Spectra
Intelligent Media Lab @ POSTECH
Motion Spectra
As does not vary across object’s surface, the power spectra of local motions across an object should have spikes at
Thus, global motion spectrum is average of power spectrum of local motions shown below.
Results in single temporal Motion Spectrum
  Advantage of using temporal spectra as features – they offer invariance to changes in scale and viewpoint.

## Slide 14: 1. Estimating Material Properties for Known Geometry
Intelligent Media Lab @ POSTECH
Vibration modes for rigid bodies are a function of length (L), diameter (d), density (ρ ) and an elastic modulus (E).
Calculates elastic modulus which gives tensile strength of the rod from modal spikes in motion spectrum of rod.
A rod’s fundamental frequency is related to its material properties as
mode

## Slide 15: Results of Rod Property Estimation
Intelligent Media Lab @ POSTECH
Estimating Properties of Materials with Known Geometry: Rods.

## Slide 16: 2. Estimating Material Properties for Unknown Geometry
Intelligent Media Lab @ POSTECH
Does not rely on knowing the ratios between resonant frequencies, which are difficult to compute in more general structures.
Learn relationships between motion spectra and the material properties of objects with regression models that map the motion spectra to the log of ground truth stiffness or area weight measurements.
Regression is performed in a lower dimensional space to avoid over-fitting (e.g. Principal Component Regression)
Setup
1)RGB SLR camera (Canon 6D, 1920×1080 px), 30 fps
2)Grayscale Point Grey camera (800×600 px), 60 fps

## Slide 17: Regression Model
Intelligent Media Lab @ POSTECH
N = 150 uniform samples of the normalized motion spectra from 0 to 15 Hz are chosen as features.
Smooth the recovered motion spectra using a Gaussian with standard deviation 15/ 2(N−1)Hz.
Fitting a regression model directly to the processed motion spectra results in overfitting.
Principal Components Regression (PCR) and Partial Least Squares Regression (PLSR).
Both methods perform comparably, suggesting that the power of our algorithm is in the features.
A leave-one-out method for training and testing.
Least Square Method Solution

## Slide 18: Results
Intelligent Media Lab @ POSTECH
Comparisons between ground truth and PCR model predictions on material properties estimated from videos of fabric excited by ambient forces and acoustic waves.
Each circle in the plots represents the estimated properties from a single video. Identical colors correspond to the same fabric.
The Pearson product-moment correlation coefficient (R-value) averaged across video samples containing the same fabric is displayed.
The features we use to estimate material properties are somewhat invariant to changes in excitation force and viewpoint

## Slide 19: Frequency sensitivity and Modes of predictions
Intelligent Media Lab @ POSTECH
Regression model has no explicit notion of resonant frequencies; it simply looks for predictive patterns in the spectra of training data.
Analyzing the sensitivity of our recovered regression models we can see which frequencies are most predictive of material properties in our fabrics.
Estimated regression coefficients
Dimensionality reducing basis vectors
Sensitivity
The sensitivity of each acoustically trained model to frequency regions in the motion spectrum. These sensitivity plots suggest that energy in the 0-5 Hz range is most predictive of a fabric’s area weight and stiffness.
By visualizing recovered mode shapes at these frequencies, we see they contain the dominant vibration modes of our fabrics.
Models use the same relationship between resonant frequencies and material properties predicted by modal analysis

## Slide 20: What we learnt
Intelligent Media Lab @ POSTECH
The rod experiments demonstrate how the technique can be used as a low cost alternative to laser vibrometers in settings that are typical for testing manufactured parts (aircraft, automobiles).
Results on fabrics demonstrate that the relationship between motion spectra and material properties can be learned, and suggests that traditional vibration analysis may be extended to applications where geometry is unknown and only loosely controlled.
Results suggest that the motion spectra we extract from video can be powerful features for scene understanding.

## Slide 21: PART ONE Deep Convolutional Neural Network for Visual Microphone/ Visual Vibrometry
Credits: Juhyun Ahn, Postech- Visual Microphone
Deblina Bhattacharjee - Visual Vibrometry

## Slide 22: Visual Microphone
Let:
Amplitude
Phase
Phase difference
(i.e. estimated displacement)
Then:
For simplicity.. Consider only one scale and orientation.
Convolution operation with weight

## Slide 23: Patch-based Visual Microphone

## Slide 24: Patch-based Visual Microphone
Similar to object classification?
Cat! (translation invariant)

## Slide 25: Tanh Activiation

## Slide 26: Convolutional Neural Network

## Slide 27: History of Motion Magnification
Magnification in presence of large motions
(Elgharib et al.) [5]
Riesz pyramid method
(Neal Wadhwa et al.) [4]
Phase-based method
(Neal Wadhwa et al.) [3]
Eulerian method
(Hao-Yu Wu et al.) [2]
Motion Magnification
(Ce Liu et al.) [1]
Year 2005
Year 2012
Year 2013
Year 2014
Year 2015
visual microphone
material property estimation from small motions
detecting pulse from head motions
personally it’s the most important algorithm
Prof. William T. Freeman @ MIT CSAIL

## Slide 28: Eulerian method
Magnification in presence of large motions [5]
Riesz pyramid method [4]
Phase-based method [3]
Eulerian method [2]
Motion Magnification [1]
problem: noise is amplified together with motion

## Slide 29: DCNN based VM
Target video frame
Current video frame
* Video is resized to [80, 80]

## Slide 30: Result
To be honest, not much difference.

## Slide 31: Result
 | Intensity Difference | Original Visual Microphone | DCVM
(Chocobox, S4) |  |  | 
(Yogurt, S6) |  |  | 
(Chips, S1) |  |  | 
Surprisingly, simply adding up the intensity difference recovered the speech. It shows that the intensity difference contains speech information.
Don't ask me to carry an oily rag like that.
Don't ask me to carry an oily rag like that.
Don't ask me to carry an oily rag like that.
Don't ask me to carry an oily rag like that.
Don't ask me to carry an oily rag like that.
She had your dark suit in greasy wash water all year.
Don't ask me to carry an oily rag like that.
She had your dark suit in greasy wash water all year.
She had your dark suit in greasy wash water all year.

## Slide 32: Problem
It fails to recover the sound after around 2,000 iterations.
Why?

## Slide 33: Problem
Post-processing
Actual recovered speech using the Visual Microphone
(normalized to [0,1])

## Slide 34: Problem
Sequence-1
Sequence-2
Sequence-3
Sequence-4
Sequence-5
Sequence-6
{chips, choco-box, yogurt, foil, tissue}
{chips, choco-box, yogurt, foil, tissue}
{chips, choco-box, yogurt, foil, tissue}
{chips, choco-box, yogurt, foil, tissue}
{chips, choco-box, yogurt, foil, tissue}
{chips, choco-box, yogurt, foil, tissue}
Not enough sequences
to train
deep neural network!!!

## Slide 35: PART TWO Improving Quality of Visual Microphone using Unsupervised Deep Bi-directional LSTM Network.

## Slide 36: Why recovered speech doesn’t sound good?
Sony RX10-3:
960fps.
- Sampling rate:
960
- Therefore by the Nyquist sampling theorem:
Maximum frequency in the recovered speech is 430Hz.
- 0~200Hz are band-pass filtered for speech signals.
Recovered speech contains only 200~430Hz speech signals.

## Slide 37: Why recovered speech doesn’t sound good?
Band-pass filtered [0Hz, 430Hz] & resampled (960fps)

## Slide 38: Why recovered speech doesn’t sound good?
?
Training can be done using normal speech sequences
– i.e. unsupervised learning!!

## Slide 39: Why recovered speech doesn’t sound good?
Actually, it is called audio bandwidth extension in signal processing community.
However, surprisingly no one has tried to solve this problem using Bi-directional LSTM network.

## Slide 40: Deep Bi-directional LSTM network
Bi-directional LSTM layer
Bi-directional LSTM layer
Bi-directional LSTM layer
Fully-connected layer
512
512
1024
257
256
256
512
512
512
1024
257

## Slide 41: TIMIT dataset
630 speakers * 10 speech files = 6,300.
Training data:
(630-3) * 10 speech files = 6,270 files.

## Slide 42: Result - English
Visual Microphone
Bandwidth Extended (1,000Hz)
Original Speech
Don't ask me to carry an oily rag like that.
Don't ask me to carry an oily rag like that.
Don't ask me to carry an oily rag like that.
She had your dark suit in greasy wash water all year.
She had your dark suit in greasy wash water all year.
She had your dark suit in greasy wash water all year.

## Slide 43: Result - Korean
Visual Microphone
Bandwidth Extended (1,000Hz)
Original Speech
아시아나 항공을 이용해주신 승객 여러분께
아시아나 항공을 이용해주신 승객 여러분께
아시아나 항공을 이용해주신 승객 여러분께
안전을 위해 좌석 벨트는 계속 매고 계시고
안전을 위해 좌석 벨트는 계속 매고 계시고
안전을 위해 좌석 벨트는 계속 매고 계시고
안에있는 물건이 떨어져 다치지 않도록
안에있는 물건이 떨어져 다치지 않도록
안에있는 물건이 떨어져 다치지 않도록

## Slide 44: Most recent work in Audio Bandwidth Extension
https://github.com/kuleshov/audio-super-res
(*NO SOURCE CODE, only demo audio files.)

## Slide 45: Appendix- Review on RNN

## Slide 46: Review on RNN

## Slide 47: Review on RNN

## Slide 48: Review on RNN

## Slide 49: Review on RNN

## Slide 50: Review on RNN

## Slide 51: Review on RNN